## Slide 1
An Overview of Tropical Cyclone Boundary Layer (TCBL) Modeling
From Meteorological Perspectives to Wind Engineering Applications
Liang Hu & Ahsan Kareem
NatHaz Modeling Laboratory, University of Notre Dame
Advances in Wind Engineering, 2025 | DOI: 10.1016/j.awe.2025.100097

## Slide 2
Outline
1. Introduction & Motivation — PBWE framework, TCBL definition
2. Full-physics TCBL Models — WRF-ARW, HWRF, HWCM, others
3. Diagnostic Models — The core of this review
  3.1 Axisymmetric models
  3.2 Parametric models: empirical & analytical
  3.3–3.6 Simulation-based: 2D-slab → 2D hybrid → 3D nonlinear (KW01)
4. Data-driven Methods — POD, ML-based approaches
5. NatHaz Systematic Investigation — Validation & applications
6. Concluding Remarks — Five research directions

## Slide 3
1. Motivation: Why TCBL Modeling?
Tropical cyclones (TCs) produce extreme near-surface winds
Performance-Based Wind Engineering (PBWE) requires accurate wind fields
  PBWE: hazard → aerodynamics → structural → damage → loss
TCBL = lowest 1–2 km of TC atmosphere — where winds impact structures
Key features: low-level jet (LLJ), supergradient winds, inflow angle
Gap: most rigorous TCBL models not yet adopted in PBWE

## Slide 4
TCBL Definition & Key Characteristics
TCBL height: typically 500–2000 m, varies with radius and azimuth
Governed by: gradient pressure, Coriolis force, surface friction, turbulent mixing
Low-level jet (LLJ): supergradient winds exceeding gradient wind by 10–25%
Inflow angle: surface wind directed inward, typically 10°–25°
Strong asymmetry: translation speed + land-sea contrast
Recent observations: GPS dropsondes, SFMR, flight-level reconnaissance

## Slide 5
TCBL Model Taxonomy
Two major groups:
  Full-physics models: NWP systems (WRF, CM1, etc.)
  — High fidelity, but too expensive for PBWE Monte Carlo
  Diagnostic models: forced by gradient profiles from track models
  — Quasi-steady solutions, computationally efficient for PBWE
Diagnostic model classification:
  Parametric (analytical) vs. Simulation-based (numerical)
  Empirical vs. Equation-solving
  Axisymmetric vs. Asymmetric | 2D vs. 3D | Linear vs. Nonlinear

## Slide 6
2. Full-physics TCBL Models
WRF-ARW: most widely used; YSU parameterization generally outperforms MYJ
  Key factors: turbulence parameterization, bottom boundary, initial conditions
  Ensemble prediction for uncertainty quantification
HWRF: operational forecasting; continuous improvements in vertical diffusion
HWCM: hybrid approach combining WRF with analytical vortex
Other models: GFS, GFDL, CM1/LES, COAMPS
Limitation: computational cost prohibits Monte Carlo simulation for PBWE
Future: accuracy & efficiency improvements may enable PBWE use

## Slide 7
3.1 Axisymmetric Models
Hybrid models (Smith 1968, Kepert 2010b)
  Parametrized vertical profiles + simulation-based solution
Height-averaged models (Smith 2003, Smith & Vogl 2008)
  Integrate primitive equations over TCBL depth → 1D ODEs
Nonlinear analytical (Kuo 1982)
  Complex variable transformation → power series solution
Linear analytical (Meng et al. 1995)
  Linearized advection → semi-analytical Ekman-type solution
  Foundation for K01 asymmetric model (wavenumber-0 component)

## Slide 8
3.2 Parametric Models (I): Empirical Methods
Gradient pressure/wind profiles:
  Axisymmetric: Holland (1980), Willoughby (2006), Emanuel (2004)
  Asymmetric: Xie et al. (2006), Georgiou (1985)
TC track models:
  Circular sub-region method, Full-track method (Vickery et al. 2000)
Vertical wind profile models:
  Surface Wind Reduction Factor (SWRF)
  TCBL profile models — empirical height-dependent adjustment

## Slide 9
3.3 Parametric Models (II): Analytical Linear
K01 model (Kepert 2001):
  3D linear asymmetric — the benchmark analytical TCBL model
  Wavenumber decomposition: wn-0 (axisymmetric) + wn-1 (translation)
Axisymmetric model accounting for asymmetry (Meng et al. 1995):
  Column model applied at each azimuth with asymmetric gradient wind
Recent developments:
  Height-dependent diffusivity, wind-dependent drag coefficients
  Semi-analytical solutions for thermal effects

## Slide 10
3.4–3.5 Simulation-based: 2D-slab & 2D Hybrid
2D-slab model:
  Height-averaged primitive equations → finite difference solution
  Widely used in PBWE (Vickery et al. 2000, Snaiki & Wu 2017)
  Limitation: no vertical structure, empirical corrections needed
2D hybrid model:
  Prescribed vertical profiles combined with 2D horizontal solution
  Bridge between 2D-slab and full 3D models

## Slide 11
3.6 The 3D Nonlinear Model (KW01) ⭐
KW01 (Kepert & Wang 2001): most rigorous diagnostic TCBL model
  Full nonlinear primitive equations in cylindrical coordinates
  Resolves vertical structure — captures LLJ, inflow angle profiles
Key physics:
  Turbulence closure: Mellor-Yamada, Louis schemes
  Vertical advection contributes ~50% of LLJ magnitude
  Landfall: land-sea roughness contrast modifies wind asymmetry
Comparison: outperforms 2D-slab and parametric models
Benchmark for evaluating all lower-level diagnostic models

## Slide 12
4. Data-driven Methods
Modifying radial profiles:
  Adjust parametric profiles using observational data
Introducing additional asymmetries:
  Beyond translation-induced: environmental shear, land effects
POD-based models:
  TARGET(t) = mean field + Σ Wi(t)·PCi
  Decompose wind fields into orthogonal modes
Promising direction: combine physics-based TCBL models with ML

## Slide 13
5. NatHaz Systematic Investigation
Goal: bridge meteorological TCBL modeling → wind engineering (PBWE)
Four components:
  (1) Model sensitivity: effects of algorithm, thermal, diffusivity, drag
  (2) Benchmark dataset: 692 sorties (Flight+ input, surface/SFMR/H*Wind output)
  (3) Hierarchy of linear models as fast approximations of KW01
  (4) Land-sea roughness contrast: ~22% overall, ~14% surface wind change

## Slide 14
6. Concluding Remarks: Five Research Directions
1. Incorporate 3D nonlinear model into PBWE
  Uncertainty quantification, alternative radial profiles, model benchmarking
2. Microscale phenomena from TCBL outputs
  Rainbands, tornado-scale vortices, urban canopy flow
3. TCBL model uncertainty → PBWE metrics
  Annual maximum wind speeds, loss ratios
4. Expand benchmark dataset
  SAR, SMAP, MTCSWA; improved dropsonde calibration
5. Data-driven model development
  ML-based asymmetry, multi-fidelity modeling, surrogates

## Slide 15
Thank You
Interactive version: peettr.github.io/tcbl-review
DOI: 10.1016/j.awe.2025.100097
Liang Hu & Ahsan Kareem NatHaz Modeling Laboratory, University of Notre Dame